## Slide 1
Secondary networks for KubeVirt VMs with DRA
DRA on kube-ovn, compared with Multus
Sören Henning · Kubermatic
KubeVirt Summit 2026

## Slide 2: Why look beyond Multus?
1
Scheduler is blind
The scheduler never sees the secondary NIC, so it cannot refuse a pod when the IP pool is full.
2
No lifecycle object
Each CNI keeps it in its own objects, like kube-ovn's IP resources. The scheduler sees none of them.
3
Serial attach
Multus calls delegate CNIs one after another, so latency grows with the number of NICs.
The question
Does DRA do better for kube-ovn's SDN NICs?

## Slide 3: From KNDM to kube-ovn
KNDM
Kubernetes Network Driver Model: declarative networking on DRA + Node Resource Interface (NRI), instead of CNI and Multus chains
DraNet
The implementation (kubernetes-sigs): discovers host devices and moves them into the pod
This work
Same DRA + NRI pattern, with an SDN backend (kube-ovn) instead of hardware
arXiv 2506.23628
Hardware backend (DraNet)
e.g. PCI NICs, SR-IOV VFs
Discovers real devices on the host
Attach = move an existing device into the netns
SDN backend (kube-ovn)
nothing to discover
The NIC is synthesized on demand
Attach = create: veth, OVS port, IP, logical port
Design principle
The controller owns allocation. The node side only plugs.

## Slide 4: kube-ovn in one slide
OVN
SDN control plane. Logical switches and routers become OVS flows on every node.
VPC
Isolated L3 domain with its own logical router.
Subnet
IP pool + L2 domain, always in exactly one VPC.
Overlay
OVN virtual network between nodes
Underlay
ProviderNetwork: a host NIC bridged into OVS, plus a Vlan for the tag
Flat IPAM
One CIDR per subnet, across all nodes
The logical switch spans every node
The scheduler picks the node, then the IP comes from the pool
Not a /27 per node like the default pod CIDR
kube-ovn-controller
Resolves device → subnet → provider
IPAM: IP + MAC, logical port, IP CR
Writes the pod annotations
GC keeps a stopped VM's ports
kube-ovn-dra-driver
Publisher: one pool per subnet, free IPs as capacity
Plugin: waits for allocated=true
Plugin: plugs the NIC (VMs: tap + DHCP)
Plugin: detaches on pod delete

## Slide 5: Control plane: the claim decides
The publisher announces the subnets and their free IPs. The claim is a scheduling input; kube-ovn allocates.
CONTROL PLANE
publisher
one pool per subnet,
free IPs as capacity
Pod / VM
+ ResourceClaim
subnetName, interfaceName
kube-scheduler
allocates a device,
binds the pod
kube-ovn-controller
IPAM, logical port, IP CR,
annotations allocated=true
OVN
logical switch
port
1
2
3
0

## Slide 6: Node: the driver only plugs
At Prepare the pod netns does not exist yet, and the NRI window is about 2 s. Hence two phases.
CONTROL PLANE
NODE
publisher
one pool per subnet,
free IPs as capacity
Pod / VM
+ ResourceClaim
subnetName, interfaceName
kube-scheduler
allocates a device,
binds the pod
kube-ovn-controller
IPAM, logical port, IP CR,
annotations allocated=true
OVN
logical switch
port
1
2
3
0
kubelet
NodePrepareResources
containerd + NRI
RunPodSandbox
kube-ovn-dra-driver
kubelet plugin: waits for
allocated=true, reads IP/MAC
NRI hook: veth into the pod,
host end on br-int
Pod netns
eth0 primary
net1 DRA NIC
OVS br-int
iface-id →
ovn-controller binds
4
5
6
7
allocated=true

## Slide 7: VMs: from tap to domain
For VMs the driver also builds the bridge, the tap and a small DHCP server. The sidecar adds the tap to the VM.
CONTROL PLANE
NODE
publisher
one pool per subnet,
free IPs as capacity
Pod / VM
+ ResourceClaim
subnetName, interfaceName
kube-scheduler
allocates a device,
binds the pod
kube-ovn-controller
IPAM, logical port, IP CR,
annotations allocated=true
OVN
logical switch
port
1
2
3
0
kubelet
NodePrepareResources
containerd + NRI
RunPodSandbox
kube-ovn-dra-driver
kubelet plugin: waits for
allocated=true, reads IP/MAC
NRI hook: veth into the pod,
host end on br-int
Pod netns
eth0 primary
net1 DRA NIC
OVS br-int
iface-id →
ovn-controller binds
4
5
6
7
allocated=true
KubeVirt binding plugin (VMs only)
adds the tap to the libvirt domain; guest gets IPv4 via DHCP
8

## Slide 8: Subnets become devices
kube-ovn Subnet
kind: Subnet
metadata:
name: ovn-subnet
spec:
cidrBlock: 10.200.0.0/24
vpc: ovn-cluster
published as
ResourceSlice (one pool per subnet)
kind: ResourceSlice
metadata:
name: nic.kubeovn.io-x7k2p
spec:
driver: nic.kubeovn.io
pool: {name: ovn-subnet}
allNodes: true
devices:
- name: subnet-ovn-subnet
allowMultipleAllocations: true
attributes:
nic.kubeovn.io/subnetName: {string: ovn-subnet}
capacity:
nic.kubeovn.io/ipv4: {value: "250"}
One pool per subnet. Overlay: all nodes. VLAN: only the nodes where its provider network is ready.
A claim selects it with CEL
device.attributes['nic.kubeovn.io']
.subnetName.stringValue == 'ovn-subnet'
A subnet is a shared IP pool, but DRA allocates exclusively by default. The 2nd pod stays Pending until the device sets AllowMultipleAllocations: true (DRAConsumableCapacity: alpha in 1.35, beta from 1.36). The free addresses are also published as capacity, so a full pool is refused at scheduling time.

## Slide 9: What live migration needs
During the migration a VM has two launcher pods. Both need the same NIC.
ResourceClaim cap-demo-vm-2-nic
named, allocated once: 172.31.0.252
source launcher pod
VM running
kube-ovn-dra-driver
prepares the claim
for the pod on this node
WORKER · SOURCE
target launcher pod
VM arrives
kube-ovn-dra-driver
prepares the claim
for the pod on this node
WORKER2 · TARGET
reservedFor
1
A named claim per VM
Source and target pod share it, so the target needs no second address. With a claim template the target pod gets its own claim, and a full pool blocks the migration.
2
The driver prepares it per node
The shared claim lists both pods. Each node prepares it for its own pod. Before the fix the target node took the source pod, and the migration hung.
3
A CNI that keeps the address
kube-ovn keeps a VM's IP and MAC across pods: the logical port is named after the VM. Not every CNI can do that.

## Slide 10: Demo: two NICs, one VM
1
make kind-demo
plus containerlab: a VLAN switch and an FRR gateway
2
kubectl get resourceslices
the published devices, one pool per subnet
3
kubectl virt ssh ubuntu@vmi/cap-demo-vm-1
one NIC on the pod network, one on the VLAN underlay
No hot-plug: NICs are attached when the sandbox starts.
VM
cap-demo-vm-1
VLAN underlay
cap-demo (VLAN 900) · DRA NIC
OVN overlay
pod network
4
ssh ubuntu@<VLAN IP>
from the kind host, through the FRR gateway
containerlab
vlan-switch · FRR gateway
kind host
ssh ubuntu@<VLAN IP>

## Slide 11: Multus vs DRA at a glance
Aspect | Multus + NAD | DRA claim
Scheduler visibility | Annotation, invisible to the scheduler. | Claim is a scheduling input. A full pool is refused at scheduling time.
Shared subnet | No concept of exclusivity. | Exclusive by default; AllowMultipleAllocations fixes it.
Lifecycle | A NAD is configuration. | A claim has allocate and release states.
Hot-plug | KubeVirt hot-plugs Multus NICs its own way. | Claims are immutable; VEP-183 non-goal.
Operations | Separate NAD and CNI chain. | One allocation path in kube-ovn-controller.
For a plain node-agnostic overlay there is no difference. For underlay, the pool of a VLAN subnet selects the nodes of its provider network.

## Slide 12: Attach time: DRA stays flat
7–12 s
DRA, 2 to 8 NICs (all 90 runs)
21 → 59 s
Multus static, +13 s per extra pair of NICs
~21 s
hot-plug: Ready with 2 NICs; 8 NICs in total ~54 s
Overlay mode, median of 10 runs; underlay and mixed within about 1 s. kind 1.35, 1 control-plane + 1 worker, homelab node.

## Slide 13: Is an SDN in scope for DRA?
1
Framework: yes
DRA doesn't care where a device comes from. This works end to end.
2
Intent: uneven
Overlay: a provisioning trigger. Underlay: node-bound pools with limited addresses.
3
Ownership: partly
An IP from a pool is a resource. Attaching to a network is configuration.
The split
Resources via DRA, configuration via a network API

## Slide 14: Where this goes next
Path into kube-ovn
Controller side
In a branch behind --enable-dra-nic, proposed upstream: kubeovn/kube-ovn#7669.
Node side
DRA kubelet plugin and NRI hook could move into kube-ovn-cni, an open question in the issue; the publisher logic can join kube-ovn-controller.
Retire
External driver, fork and binding sidecar.
API gaps in multi-network-api
Network → DeviceClass binding
Interface-name ownership (net1, net2, …)
A standard network-capacity signal (published per subnet here)
Moving in parallel
KNDM / DraNet: the same DRA + NRI model; kube-ovn adds the SDN backend
KubeVirt VEP-183: ResourceClaim as a VM network source
multi-network-api: NetworkKind vs PodNetwork, both built on DRA

## Slide 15: Takeaways
1
Complementary, not a verdict
Multus and DRA differ in visibility, IP handling and lifecycle.
2
On an SDN, the work is in the control plane
The node side is thin.
3
So it belongs in kube-ovn
Controller first, node side later, in one release.
github.com/soer3n/kube-ovn-dra-driver
github.com/soer3n/kube-ovn-network-binding-plugin
Questions and feedback welcome in the issue, or on Slack: @soer3n
Discussion upstream
kubeovn/kube-ovn#7669